_____[ 1 ]___[ 12:08:11,078 ]___[ DOWN ]____[ SDCCH ]______________________________

13 05 04 07 a1 88 89 21 15 63 e0 5c 08 11 83 94 33 57 92 28 f1

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

05  00------  SendSequenceNumber  : 0

--000101  MESSAGE TYPE        : SETUP

04  00000100  INFORMATION ELEMENT : Bearer capability

07  00000111  length              : 7

a1  1-------  Extension           : 1

-01-----  Radio Channel Req.  : full rate support only MS

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----001  Info Transfer Cap.  : unrestricted digital information

88  1-------  Extension           : 1

-0------  Compression         : data compression not possible

--00----  Structure           : service data unit integrity

----1---  Duplex Mode         : full duplex

-----0--  Configuration       : point-to-point

------0-  Negot. of Int.      : No meaning is associated with this value.

-------0  Establishment       : demand

89  1-------  Extension           : 1

-00-----  Access ID           : octet identifier

---01---  Rate Adaptation     : V.110/X.30

-----001  Signalling Acc.Prot : I.440/450

21  0-------  Extension           : 0

-01-----  Layer 1 ID

---0000-  User Info L1 Prot   : Default layer1 protocol

-------1  Sync/async          : asynchronous

15  0-------  Extension           : 0

-0------  Numb Stop Bits      : 1 bit (also used in the case of synchr mode)

--0-----  Negotiation         : in-band negotiation not possible

---1----  Numb Data Bits      : 8 bits (also used i case of bit oriented protocols)

----0101  User Rate           : 9.6 kbit/sRecommendation X.1 and V.110

63  0-------  Extension           : 0

-11-----  Intermediate Rate   : 16 kbit/s

---0----  NIC On Tx           : not require to send data with network  indep.clock

----0---  NIC On Rx           : can't accept data with network indep. clock

-----011  Parity              : none

e0  1-------  Extension           : 1

-11-----  Connect Element     : both, non transparent preferred

---00000  Modem Type          : none

5c  01011100  INFORMATION ELEMENT : Calling party BCD number

08  00001000  length              : 8

11  0-------  Extension           : 0

-001----  Type of number      : international number

----0001  Numb. plan id.      : ISDN/telephony numb. pl. (Rec. E.164/E.163)

83  1-------  Extension           : 1

-00-----  Present.indic.      : Presentation allowed

---000--  spare               : 0

------11  Present.indic.      : Network provided

94..f1        number              : 49337529821

_____[ 2 ]___[ 12:08:11,078 ]___[ UP ]___________________________________________

93 08 04 07 a1 88 89 21 15 63 a0

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

08  00------  SendSequenceNumber  : 0

--001000  MESSAGE TYPE        : CALL CONFIRMED

04  00000100  INFORMATION ELEMENT : Bearer capability

07  00000111  length              : 7

a1  1-------  Extension           : 1

-01-----  Radio Channel Req.  : full rate support only MS

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----001  Info Transfer Cap.  : unrestricted digital information

88  1-------  Extension           : 1

-0------  Compression         : data compression not possible

--00----  Structure           : service data unit integrity

----1---  Duplex Mode         : full duplex

-----0--  Configuration       : point-to-point

------0-  Negot. of Int.      : No meaning is associated with this value.

-------0  Establishment       : demand

89  1-------  Extension           : 1

-00-----  Access ID           : octet identifier

---01---  Rate Adaptation     : V.110/X.30

-----001  Signalling Acc.Prot : I.440/450

21  0-------  Extension           : 0

-01-----  Layer 1 ID

---0000-  User Info L1 Prot   : Default layer1 protocol

-------1  Sync/async          : asynchronous

15  0-------  Extension           : 0

-0------  Numb Stop Bits      : 1 bit (also used in the case of synchr mode)

--0-----  Negotiation         : in-band negotiation not possible

---1----  Numb Data Bits      : 8 bits (also used i case of bit oriented protocols)

----0101  User Rate           : 9.6 kbit/sRecommendation X.1 and V.110

63  0-------  Extension           : 0

-11-----  Intermediate Rate   : 16 kbit/s

---0----  NIC On Tx           : not require to send data with network  indep.clock

----0---  NIC On Rx           : can't accept data with network indep. clock

-----011  Parity              : none

a0  1-------  Extension           : 1

-01-----  Connect Element     : non transparent (RLP)

---00000  Modem Type          : none

_____[ 3 ]___[ 12:08:12,949 ]___[ UP ]____[ FACCH_F ]______________________________

93 01

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

01  00------  SendSequenceNumber  : 0

--000001  MESSAGE TYPE        : ALERTING

_____[ 4 ]___[ 12:08:19,102 ]___[ UP ]____[ SACCH ]______________________________

93 25 02 e0 91

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

25  00------  SendSequenceNumber  : 0

--100101  MESSAGE TYPE        : DISCONNECT

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

91  -0010001  cause               : User busy

_____[ 5 ]___[ 12:08:19,430 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 2d 08 02 e0 91

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2d  00------  SendSequenceNumber  : 0

--101101  MESSAGE TYPE		: RELEASE

08  00001000  INFORMATION ELEMENT	: Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

91  -0010001  cause               : User busy

_____[ 6 ]___[ 12:08:19,430 ]___[ UP ]___________________________________________

93 2a 08 02 e0 91

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2a  00------  SendSequenceNumber  : 0

--101010  MESSAGE TYPE        : RELEASE COMPLETE

08  00001000  INFORMATION ELEMENT : Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

91  -0010001  cause               : User busy