_____[ 1 ]___[ 15:32:06,402 ]___[ UP ]___________________________________________

05 24 01 03 23 19 01 05 f4 31 e0 9f 55

05  0-------  direction from      : originating site

-000----  TransactionID       : 0

----0101  Protocol Discrim.   : mobile management messages non GPRS

24  00------  SendSequenceNumber  : 0

--100100  MESSAGE TYPE        : CM SERVICE REQUEST

01  0-------  spare               : 0

-000----  value for the ciphering key sequence number = 0

----0001  Requ.service type   : Mobile originating call establishment, or packet mode connection establishment

: Mobile Station Classmark 2

03  00000011  length              : 3

23  0-------  1 spare             : 0

-01-----  Revision Level      : Used by phase 2 mobile stations

---0----  "Controlled Early Classmark Sending" option is not implemented in the MS

----0---  Encryp.Algor. A5_1  : available

-----011  RF power capability : Class 4, handheld

19  0-------  1 spare bit         : 0

-0------  pseudo-synch.capab. : not present

--01----  SS Screening Indic. : phase 2 error handling

----1---  Mobile station supports mobile terminated point to point SMS

-----0--  no VoiceBroadcastService (VBS) capability or no notifications wanted

------0-  no VoiceGroupCallService (VGCS) capability or no notifications wanted

-------1  The MS does support the E-GSM or R-GSM

01  0-------  The MS does not support any options that are indicated in CM3

-0------  1 spare bit         : 0

--0-----  LocationServiceValueAdded Capability  not supported

---0----  1 spare bit         : 0

----0---  SoLSA Capability    : not supported

-----0--  Network initiated MO CM connection request not supported.

------0-  encryp.algorith.A5/3: not available

-------1  encryp.algorith.A5/2: available

: Mobile identity

05  00000101  length              : 5

f4  ----0---  No. of ID digits     : even

-----100  Type of identity     : TMSI/P-TMSI

1111----  Identity Digit 1     : 95

31  00110001  Identity Digit 2,3  : take hex value

e0  11100000  Identity Digit 4,5  : take hex value

9f  10011111  Identity Digit 6,7  : take hex value

55  01010101  Identity Digit 8,9  : take hex value

_____[ 2 ]___[ 15:32:08,574 ]___[ UP ]___________________________________________

03 05 04 04 60 02 00 81 5e 08 91 94 33 57 12 80 51 f6 a2

03  0-------  direction from      : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

05  00------  SendSequenceNumber  : 0

--000101  MESSAGE TYPE        : SETUP

04  00000100  INFORMATION ELEMENT : Bearer capability

04  00000100  length              : 4

60  0-------  Extension           : 0

-11-----  Radio Channel Req.  : dual rate support MS/full rate preferred

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----000  Info Transfer Cap.  : speech

02  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0010  speech Vers. indic. : GSM full rate speech version 2

00  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0000  speech Vers. indic. : GSM full rate speech version 1

81  1-------  Extension           : 1

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0001  speech Vers. indic. : GSM half rate speech version 1

5e  01011110  INFORMATION ELEMENT : CalledPartyBCDNumber

08  00001000  length              : 8

91  1-------  Extension           : 1

-001----  Type of number      : international number

----0001  Numb. plan id.      : ISDN/teleph. numb. plan (Rec. E.164/E.163) _

94..f6        number              : 4933752108156

a2  10100010  Information Element : CLIR Invocation

_____[ 3 ]___[ 15:32:09,496 ]___[ DOWN ]____[ SDCCH ]______________________________

83 02

83  1-------  direction to        : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

02  00------  SendSequenceNumber  : 0

--000010  MESSAGE TYPE        : CALL PROCEEDING

_____[ 4 ]___[ 15:32:12,039 ]___[ DOWN ]____[ FACCH_F ]______________________________

83 01 1e 02 ea 88

83  1-------  direction to        : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

01  00------  SendSequenceNumber  : 0

--000001  MESSAGE TYPE        : ALERTING

1e  00011110  INFORMATION ELEMENT : Progress indicator

02  00000010  L. OF IE PROG.IND.  : 2

ea  1-------  Extension           : 1

-11-----  Coding standard     : Stand. Def. for the GSM-PLMNS as descry.

---0----  Spare               : 0

----1010  Location            : Network beyond interworking point

88  1-------  Extension           : 1

-0001000  Progress descr.     : In-band inform. or appr. pattern now available

_____[ 5 ]___[ 15:32:15,816 ]___[ UP ]____[ SACCH ]______________________________

03 25 02 e0 90

03  0-------  direction from      : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

25  00------  SendSequenceNumber  : 0

--100101  MESSAGE TYPE        : DISCONNECT

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 6 ]___[ 15:32:16,125 ]___[ DOWN ]____[ FACCH_F ]______________________________

83 2d 08 02 e0 90

83  1-------  direction to        : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

2d  00------  SendSequenceNumber  : 0

--101101  MESSAGE TYPE		: RELEASE

08  00001000  INFORMATION ELEMENT	: Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 7 ]___[ 15:32:16,125 ]___[ UP ]___________________________________________

03 2a

03  0-------  direction from      : originating site

-000----  TransactionID       : 0

----0011  Protocol Discrim.   : Call control and call related SS messages

2a  00------  SendSequenceNumber  : 0

--101010  MESSAGE TYPE        : RELEASE COMPLETE