_____[ 1 ]___[ 11:59:52,632 ]___[ DOWN ]____[ SDCCH ]______________________________

13 05 04 07 a3 b8 81 20 15 63 80 5c 08 11 83 94 33 57 92 28 f1 7d 02 91 84

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

05  00------  SendSequenceNumber  : 0

--000101  MESSAGE TYPE        : SETUP

04  00000100  INFORMATION ELEMENT : Bearer capability

07  00000111  length              : 7

a3  1-------  Extension           : 1

-01-----  Radio Channel Req.  : full rate support only MS

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----011  Info Transfer Cap.  : facsimile group 3

b8  1-------  Extension           : 1

-0------  Compression         : data compression not possible

----1---  Duplex Mode         : full duplex

-----0--  Configuration       : point-to-point

------0-  Negot. of Int.      : No meaning is associated with this value.

-------0  Establishment       : demand

81  1-------  Extension           : 1

-00-----  Access ID           : octet identifier

---00---  Rate Adaptation     : no rate adaption

-----001  Signalling Acc.Prot : I.440/450

20  0-------  Extension           : 0

-01-----  Layer 1 ID

---0000-  User Info L1 Prot   : Default layer1 protocol

-------0  Sync/async          : synchronous

15  0-------  Extension           : 0

-0------  Numb Stop Bits      : 1 bit (also used in the case of synchr mode)

--0-----  Negotiation         : in-band negotiation not possible

---1----  Numb Data Bits      : 8 bits (also used i case of bit oriented protocols)

----0101  User Rate           : 9.6 kbit/sRecommendation X.1 and V.110

63  0-------  Extension           : 0

-11-----  Intermediate Rate   : 16 kbit/s

---0----  NIC On Tx           : not require to send data with network  indep.clock

----0---  NIC On Rx           : can't accept data with network indep. clock

-----011  Parity              : none

80  1-------  Extension           : 1

-00-----  Connect Element     : transparent

---00000  Modem Type          : none

5c  01011100  INFORMATION ELEMENT : Calling party BCD number

08  00001000  length              : 8

11  0-------  Extension           : 0

-001----  Type of number      : international number

----0001  Numb. plan id.      : ISDN/telephony numb. pl. (Rec. E.164/E.163)

83  1-------  Extension           : 1

-00-----  Present.indic.      : Presentation allowed

---000--  spare               : 0

------11  Present.indic.      : Network provided

94..f1        number              : 49337529821

7d  01111101  INFORMATION ELEMENT : High Layer Compatibility

02  00000010  length              : 2

91  1-------  Extension           : 1

-00-----  Coding standard     : CCITT standardized coding

---100--  Interpret.i.ch.     : First high layer char.id. to be used

------01  Present.method      : High Layer protocol profile

84  10000100  High layer char.    : Facsimile Group 2/3

_____[ 2 ]___[ 11:59:52,632 ]___[ UP ]___________________________________________

93 08

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

08  00------  SendSequenceNumber  : 0

--001000  MESSAGE TYPE        : CALL CONFIRMED

_____[ 3 ]___[ 11:59:54,465 ]___[ UP ]____[ FACCH_F ]______________________________

93 01

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

01  00------  SendSequenceNumber  : 0

--000001  MESSAGE TYPE        : ALERTING

_____[ 4 ]___[ 12:00:10,877 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 3a 10 a1 0e 02 01 01 02 01 10 30 06 81 01 2a 85 01 02

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

3a  00------  SendSequenceNumber  : 0

--111010  MESSAGE TYPE        : FACILITY

10  00010000  Lgth OF IE FACILITY : 16

a1  10100001  Component           : Invoke

0e  00001110  length              : 14

02  00000010  Type=INTEGER        : Invoke Identifier

01  00000001  length              : 1

01  00000001  Inv.ID. Value       : 1

02  00000010  Type=INTEGER        : Operation Value

01  00000001  length              : 1

10  00010000  OperationValue      : notifySS

30  00110000  Type=SEQUENCE       : Operation

06  00000110  length              : 6

81  10000001  IMPL.OCTETSTRING    : ss-code

01  00000001  length              : 1

2a  00101010  ss-code Value       : cfnry

85  10000101  IMPL.OCTETSTRING    : SS-Notification

01  00000001  length              : 1

02  ------1-  incoming call has been forwarded to C

_____[ 5 ]___[ 12:00:10,027 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 2d 08 02 e2 9f

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2d  00------  SendSequenceNumber  : 0

--101101  MESSAGE TYPE		: RELEASE

08  00001000  INFORMATION ELEMENT	: Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e2  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0010  location            : public network serving the local user

9f  -0011111  cause               : Normal, unspecified

_____[ 6 ]___[ 12:00:10,027 ]___[ UP ]___________________________________________

93 2a 08 02 e0 9f

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2a  00------  SendSequenceNumber  : 0

--101010  MESSAGE TYPE        : RELEASE COMPLETE

08  00001000  INFORMATION ELEMENT : Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

9f  -0011111  cause               : Normal, unspecified