_____[ 1 ]___[ 10:48:25,715 ]___[ DOWN ]____[ SDCCH ]______________________________

13 05 04 01 a0 5c 09 11 81 94 33 57 12 80 51 f6 7d 02 91 81

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

05  00------  SendSequenceNumber  : 0

--000101  MESSAGE TYPE        : SETUP

04  00000100  INFORMATION ELEMENT : Bearer capability

01  00000001  length              : 1

a0  1-------  Extension           : 1

-01-----  Radio Channel Req.  : full rate support only MS

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----000  Info Transfer Cap.  : speech

5c  01011100  INFORMATION ELEMENT : Calling party BCD number

09  00001001  length              : 9

11  0-------  Extension           : 0

-001----  Type of number      : international number

----0001  Numb. plan id.      : ISDN/telephony numb. pl. (Rec. E.164/E.163)

81  1-------  Extension           : 1

-00-----  Present.indic.      : Presentation allowed

---000--  spare               : 0

------01  Present.indic.      : User-provided, verified and passed

94..f6        number              : 4933752108156

7d  01111101  INFORMATION ELEMENT : High Layer Compatibility

02  00000010  length              : 2

91  1-------  Extension           : 1

-00-----  Coding standard     : CCITT standardized coding

---100--  Interpret.i.ch.     : First high layer char.id. to be used

------01  Present.method      : High Layer protocol profile

81  10000001  High layer char.    : Telephony

_____[ 2 ]___[ 10:48:25,715 ]___[ UP ]___________________________________________

93 08 04 04 60 02 00 81

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

08  00------  SendSequenceNumber  : 0

--001000  MESSAGE TYPE        : CALL CONFIRMED

04  00000100  INFORMATION ELEMENT : Bearer capability

04  00000100  length              : 4

60  0-------  Extension           : 0

-11-----  Radio Channel Req.  : dual rate support MS/full rate preferred

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----000  Info Transfer Cap.  : speech

02  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0010  speech Vers. indic. : GSM full rate speech version 2

00  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0000  speech Vers. indic. : GSM full rate speech version 1

81  1-------  Extension           : 1

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0001  speech Vers. indic. : GSM half rate speech version 1

_____[ 3 ]___[ 10:48:26,836 ]___[ UP ]____[ FACCH_F ]______________________________

93 01

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

01  00------  SendSequenceNumber  : 0

--000001  MESSAGE TYPE        : ALERTING

_____[ 4 ]___[ 10:48:31,691 ]___[ UP ]____[ SACCH ]______________________________

93 07

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

07  00------  SendSequenceNumber  : 0

--000111  MESSAGE TYPE        : CONNECT

_____[ 5 ]___[ 10:48:31,953 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 0f

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

0f  00------  SendSequenceNumber  : 0

--001111  MESSAGE TYPE        :CONNECT ACKNOWLEDGE

_____[ 6 ]___[ 10:48:41,695 ]___[ DOWN ]____[ FACCH_F ]______________________________

23 05 04 01 a0 34 07 5c 08 11 81 94 33 57 92 28 f1 7d 02 91 81

23  0-------  direction from      : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

05  00------  SendSequenceNumber  : 0

--000101  MESSAGE TYPE        : SETUP

04  00000100  INFORMATION ELEMENT : Bearer capability

01  00000001  length              : 1

a0  1-------  Extension           : 1

-01-----  Radio Channel Req.  : full rate support only MS

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----000  Info Transfer Cap.  : speech

34  00110100  Information Element : SIGNAL

: Signal value

07  00000111  call waiting tone on

5c  01011100  INFORMATION ELEMENT : Calling party BCD number

08  00001000  length              : 8

11  0-------  Extension           : 0

-001----  Type of number      : international number

----0001  Numb. plan id.      : ISDN/telephony numb. pl. (Rec. E.164/E.163)

81  1-------  Extension           : 1

-00-----  Present.indic.      : Presentation allowed

---000--  spare               : 0

------01  Present.indic.      : User-provided, verified and passed

94..f1        number              : 49337529821

7d  01111101  INFORMATION ELEMENT : High Layer Compatibility

02  00000010  length              : 2

91  1-------  Extension           : 1

-00-----  Coding standard     : CCITT standardized coding

---100--  Interpret.i.ch.     : First high layer char.id. to be used

------01  Present.method      : High Layer protocol profile

81  10000001  High layer char.    : Telephony

_____[ 7 ]___[ 10:48:41,695 ]___[ UP ]___________________________________________

a3 08 04 04 60 02 00 81 08 02 e0 91

a3  1-------  direction to        : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

08  00------  SendSequenceNumber  : 0

--001000  MESSAGE TYPE        : CALL CONFIRMED

04  00000100  INFORMATION ELEMENT : Bearer capability

04  00000100  length              : 4

60  0-------  Extension           : 0

-11-----  Radio Channel Req.  : dual rate support MS/full rate preferred

---0----  Coding Standard     : GSM standard coding

----0---  Transfer Mode       : Circuit Mode

-----000  Info Transfer Cap.  : speech

02  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0010  speech Vers. indic. : GSM full rate speech version 2

00  0-------  Extension           : 0

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0000  speech Vers. indic. : GSM full rate speech version 1

81  1-------  Extension           : 1

-0------  Coding              : octet used for extension of inf. transf. capab.

--00----  Spare               : 00

----0001  speech Vers. indic. : GSM half rate speech version 1

_____[ 8 ]___[ 10:48:41,809 ]___[ UP ]____[ FACCH_F ]______________________________

a3 01

a3  1-------  direction to        : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

01  00------  SendSequenceNumber  : 0

--000001  MESSAGE TYPE        : ALERTING

_____[ 9 ]___[ 10:48:55,637 ]___[ UP ]____[ SACCH ]______________________________

93 18

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

18  00------  SendSequenceNumber  : 0

--011000  MESSAGE TYPE        : HOLD

_____[ 10 ]___[ 10:48:55,867 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 19

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

19  00------  SendSequenceNumber  : 0

--011001  MESSAGE TYPE        : HOLD ACKNOWLEDGE

_____[ 11 ]___[ 10:48:55,867 ]___[ UP ]___________________________________________

a3 07

a3  1-------  direction to        : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

07  00------  SendSequenceNumber  : 0

--000111  MESSAGE TYPE        : CONNECT

_____[ 12 ]___[ 10:48:56,137 ]___[ DOWN ]____[ FACCH_F ]______________________________

23 0f

23  0-------  direction from      : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

0f  00------  SendSequenceNumber  : 0

--001111  MESSAGE TYPE        :CONNECT ACKNOWLEDGE

_____[ 13 ]___[ 10:49:13,152 ]___[ UP ]___________________________________________

93 3a 08 a1 06 02 01 01 02 01 7c 7f 01 00

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

3a  00------  SendSequenceNumber  : 0

--111010  MESSAGE TYPE        : FACILITY

08  00001000  Lgth OF IE FACILITY : 8

a1  10100001  Component           : Invoke

06  00000110  length              : 6

02  00000010  Type=INTEGER        : Invoke Identifier

01  00000001  length              : 1

01  00000001  Inv.ID. Value       : 1

02  00000010  Type=INTEGER        : Operation Value

01  00000001  length              : 1

7c  01111100  Operation Value     : buildMPTY

_____[ 14 ]___[ 10:49:13,902 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 3a 05 a2 03 02 01 01

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

3a  00------  SendSequenceNumber  : 0

--111010  MESSAGE TYPE        : FACILITY

05  00000101  Lgth OF IE FACILITY : 5

a2  10100010  Component           : ReturnResult

03  00000011  length              : 3

02  00000010  Type=INTEGER        : Invoke Identifier

01  00000001  length              : 1

01  00000001  Inv.ID. Value       : 1

_____[ 15 ]___[ 10:49:25,770 ]___[ UP ]____[ SACCH ]______________________________

93 25 02 e0 90

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

25  00------  SendSequenceNumber  : 0

--100101  MESSAGE TYPE        : DISCONNECT

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 16 ]___[ 10:49:25,809 ]___[ UP ]____[ FACCH_F ]______________________________

a3 25 02 e0 90

a3  1-------  direction to        : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

25  00------  SendSequenceNumber  : 0

--100101  MESSAGE TYPE        : DISCONNECT

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 17 ]___[ 10:49:26,039 ]___[ DOWN ]____[ FACCH_F ]______________________________

13 2d 08 02 e0 90

13  0-------  direction from      : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2d  00------  SendSequenceNumber  : 0

--101101  MESSAGE TYPE		: RELEASE

08  00001000  INFORMATION ELEMENT	: Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 18 ]___[ 10:49:26,039 ]___[ UP ]___________________________________________

93 2a

93  1-------  direction to        : originating site

-001----  TransactionID       : 1

----0011  Protocol Discrim.   : Call control and call related SS messages

2a  00------  SendSequenceNumber  : 0

--101010  MESSAGE TYPE        : RELEASE COMPLETE

_____[ 19 ]___[ 10:49:26,230 ]___[ DOWN ]____[ FACCH_F ]______________________________

23 2d 08 02 e0 90

23  0-------  direction from      : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

2d  00------  SendSequenceNumber  : 0

--101101  MESSAGE TYPE		: RELEASE

08  00001000  INFORMATION ELEMENT	: Cause

02  00000010  LENGTH OF IE CAUSE  : 2

e0  1-------  Extension Bit       : 1

-11-----  Coding stand.       : Standard defined for the GSM-PLMNS

---0----  spare               : 0

----0000  location            : user

90  -0010000  cause               : Normal call clearing

_____[ 20 ]___[ 10:49:26,230 ]___[ UP ]___________________________________________

a3 2a

a3  1-------  direction to        : originating site

-010----  TransactionID       : 2

----0011  Protocol Discrim.   : Call control and call related SS messages

2a  00------  SendSequenceNumber  : 0

--101010  MESSAGE TYPE        : RELEASE COMPLETE